CESSNA 152 ABBREVIATED CHECKLIST

| INTERNAL CHECKS | Suction | More than 3” |
| --- | --- | --- |
| Passenger brief | Completed | Radio/Nav | ON |
| Seats & belts | Adjusted & secure | Instruments | Set DI & AI erected |
| Door & window | Check | Flaps | Check all stages then UP |
| Parking brake | On | Magnetos | Check |
| Instruments | Undamaged, legible & secure | TAXYING |
| Cabin air / heat | Free movement - OFF | Brakes | Check |
| Fuel | ON, confirm endurance | Rudder | Check steering |
| CB’s | Check IN | Flight instruments | Check: DI, Compass, AI & TC |
| Trim | Check full & free, set for T/O | POWER CHECKS |  |
| Controls | Full & free | Position | Into wind, secure area |
| Mixture | Full & free, set RICH | Brakes | ON |
| Throttle | Full & free, set ¼” open | Oil | T’s & P’s in limits |
| Carb. Heat | Full & free, set COLD | RPM | 1700 |
| Master switch | On, Nav lights ON at night | Carb. heat | Hot, 50 RPM drop max, COLD |
| Radio | On, obtain ATIS | Magnetos | Check, max drop 125 |
| Radio | OFF |  | Max diff 50 RPM |
| Altimeter(s) | Set | Suction | 4.5-5.4” HG |
| Beacon | ON | Ammeter | Charging |
| Prime | As required & LOCK | Oil | T’s & P’s in limits |
| STARTING |  | Idle | Close, 500-700 RPM |
| Key | In, Mags OFF |  | T’s & P’s in limits Ammeter dis. |
| Lookout | Check & call CLEAR PROP | RPM | Set 1200 |
| Magneto | Start, hand on throttle | SPEEDS (Kts) |  |
| AFTER START |  | Vr | 50 |
| Starter WNG light | OUT | Vy 10°Flap / No Flap | 60 / 65 |
| Oil pressure | Rising within 30 sec/Shut down | Glide | 65 |
| RPM | Set 1200 | Vat (30° flap) | 55 |
| Ammeter | Charging | X wind | 12 |

| PRE TAKE-OFF CHECKS | AFTER LANDING |  |
| --- | --- | --- |
| Trim | Set for T/O | Carb. heat | Cold |
| Throttle friction | Finger tight | Flaps | Up |
| Mixture | Rich | Pitot heat | Off |
| Magnetos | On BOTH | Strobe / landing lights | Off |
| Master switch | ON | Transponder | Standby |
| Fuel | ON, confirm endurance | Non-essential electrics | Off |
| Flaps | As required | SHUT DOWN |  |
| Gauges | T’s & P’s in limits | Park | Nose wheel straight |
| Instruments | DI, ALT, Radio nav aids as req. | Brake | Apply |
| Harness | Secure | Engine | 1200 RPM, check T’s & P’s |
| Hatches | Doors & windows closed | Magnetos | Check |
| Controls | Full & free | Radios (inc. Tx) | OFF |
| Take-off brief | Review speeds | Mixture | ICO |
| AFTER TAKE-OFF |  | After engine stop: |
| Lookout | Check drift | Magnetos | OFF, key out |
| Flaps | Retract after 300’ | Nav lights | OFF |
| Oil | T’s & P’s in limits | Beacon | Leave ON |
| CRUISE |  | Master switch | Off |
| Power | Set RPM (22 / 2300) | Fuel | Leave On |
| Trim | Set | Control lock | In |
| Mixture | Lean | Harness | Tidy |
| FREDA |  | External | Pitot cover, tie downs, chocks |
| Fuel | Confirm endurance | FUEL CAPACITY (Normal tanks) |
| Radio/radio aids | Check, set as req. | Total capacity | 21.7 Imp G | 99 L |
| Engine | Carb.heat: HOT, RPM drop | Useable fuel | 20.5 Imp G | 93 L |
|  | T’s & P’s in limits | OIL |
|  | Mixture | Min / normal | 4 qts | 6 qts |
|  | Suction & charging |  |  |
|  | Carb. heat COLD, RPM restored |  |  |
| DI | Check |  |  |
| ALT | Check |  |  |